## Slide 1: Online Hierarchical Conformance Refinement Planning for Intelligent Autonomous Mobile Robots using Answer Set Programming
Oliver Michael Kamperis
Supervisors: Marco Castellani and Yongjing Wang

## Slide 2: The Objective
Objective is to obtain a planner effective for very capable robots, that will be deployed into real-world domains, including our homes or work places, to do general tasks previously done only by humans.
This thesis tackles the problem of plan generation in such domains,
This needs a general method that is fast and finds good quality plans.
Planning time and execution latency must be very small to be useful;
  Search space explodes exponentially with plan length in exhaustive search,
  Hard to avoid this and still get good quality plans for complex problems,
  Even harder to find method that doesn’t use problem specific knowledge.
Notes: So things like cooking and cleaning, or stacking shelves, packing bags at a shopping market, things that require a really general capacity to understand and reason about the world.
These are domains that demand the ability to plan, and where we can’t rely solely on reactive decision making.
The problems and issues faced with change on a daily basis
We are willing to give up some extent of plan quality, if we are able to get a plan at all, and particularly if we are able to get a plan extremely quickly.
Really, we need the robot to be able to start executing in a few seconds.
We want it to at the very least, generalise over different problems in the same domain.

## Slide 3: ASP Based Planning
ASP is a knowledge representation and reasoning language;
  Highly expressive and general for modelling and solving problems,
  Easy to write and expand encodings (very good elaboration tolerance).
Fundamental physical laws of a system written as logical axioms;
  Effects - “Moving changes your location and/or orientation”,
  Conditions - “You can only move between locations that are connected”,
  Constraints - “An object you are grasping always shares your location”.
Performs well for problems with many complex interacting constraints and large number of relevant entity constants,
Performs poorly for problems with long minimal plan lengths.
Notes: These axioms are intuitive to write by a human, and there is existing work that shows these can be learnt by logical induction.
In contrast, most other planning languages can’t use axiomatic representations, particularly you can’t express state constraints, usually just static effects and preconditions.
Unfortunately, many complex problems do have long plan lengths,
To date, there aren’t any ASP based planners that are effective for any real-world uses, as they are intractable for most non-trivial problems.

## Slide 4: Classical Heuristic Planning
Classical heuristic planners have contrasting strengths to ASP.
Heuristic planners use predictive model to estimate cost to goal;
  Used to avoid searching most of the space of possible plans,
  Resultantly can (usually) deal with long plan lengths very efficiently.
They require ability to get accurate heuristic estimate efficiently;
  Some trivially measured property of the domain (e.g. literal distance to goal),
  Elaborate predictive models that will generalise to more complex problems.
Only effective for real-world problems, if they are dealing with a limited representation, that allows the heuristic to work effectively.
Not as expressive or general as ASP, often poor elaboration tolerance.
Notes: This is because heuristics can massively reduce the potential search space, but in order to achieve this, the expressiveness of the encoding has to be limited to allow the heuristic to reason about properties that will exist in all possible encodings in a general manner,
This is a design choice, heuristic planners have clear strengths and weaknesses, and these have been studied extensively.

## Slide 5: Comparison
ASP appears to have the capabilities to achieve our objective;
  Well suited at representing complex problems with desired generality,
  But these tend to have plan lengths that are too long for it to deal with.
Heuristic planners beat ASP for problems that are simple enough to get accurate heuristic estimates, or when a lot of prior knowledge of the problem is available, even when plan lengths are very long.
We can’t rely on heuristics to enhance ASP for multiple reasons;
  Types of problems ASP used for are too complex to rely on heuristic guidance only,
  Heuristics can make the logic program exponentially larger,
  Even if we can find one, we might lose the desired generality.
If we want the benefits of ASP we need some alternative way of dealing with these long plans and high planning complexity.
Notes: There are some pretty conclusive existing studies that show that ASP generally out performs the most efficient classical planners available for such problems, especially when there are large amounts of relevant entity constants, because it is extremely good at dealing with large knowledge bases.
But, for problems that are tractable for classical planners, but have long plan lengths, ASP usually doesn’t perform very well, because it cannot handle the exponential explosion in the search space was well as classical planners can if they have an effective heuristic.
If we want to get robots into complex real-world domains, we need to start looking at alternative approaches.
A lot of research looks towards human reasoning techniques for inspiration, chief among these are machine learning based approaches which used prior experience to inform planning, and there are a large variety of approaches in the field, the others are those based on abstractions, these have generally been used in two ways, heuristics and hierarchical planning.
Using heuristics seems counter-intuitive to what we want.
There is no reason why we can’t use learnt knowledge from previous experience to help us for similar problems encountered in the future – this is exactly what humans do – but we also need to be able to represent domain knowledge more precisely and elegantly – in a human like manner also – and we need to be general enough to be able to solve problems we have not seen before.
In other words, we want to be fast enough to be useful when dealing with tasks/problems we have not seen before, but we also want to be flexible enough to integrate any existing prescriptive knowledge if available.

## Slide 6: Hierarchical Refinement Planning
In place of a heuristic an abstraction hierarchy is used,
Refines abstract plans down an abstraction hierarchy to progressively divide and sub-divide problems into smaller sub-problems;
  Divide-and-conquer can exponentially reduce plan lengths and planning complexity,
  Good where obtaining an accurate heuristic estimate too difficult or expensive.
However, existing planners only support relaxed and reduced models;
  These are not always appropriate for all domain/problems,
  Relaxed models can make planning harder if branching factors are increased.
Planning time and plan quality can be exponentially worse;
  Not always an effective way to divide a given problem,
  If sub-problems are not independent plans can approach exponentially longer.
Notes: This an alternative approach to classical heuristic planning for reducing planning complexity, particularly for complex problems with long plan lengths.
Good for complex problems, were there isn’t a clear measure to the goal, were there are clear abstractions to be made.
Essentially, not always possible to build a hierarchy that will work for a given domain, because we are limited to just one type of abstraction.
It happens very often that when you divide a problem, those parts will end up being dependent upon each other, and because they have to be considered separately the solution to one sub-problem, might leave the planner in a state that makes it harder to solve the next sub-problem.
The speed comes from the problem division only, which requires that every action to be refined as a separate sub-problem, unfortunately each sub-problem is often far from independent and the resulting sub-plans can approach exponentially longer.
Still limited to classical planning, usually only allows static effects and preconditions, no conditionals, or state constraints/relations.

## Slide 7: The Proposed Approach
ASP based and refinement planning have complimentary strengths, this thesis seeks to show they overcomes weaknesses of each other.
  ASP very well suited to representing abstraction hierarchies,
  Refinement very well suited to dealing with long plan lengths.
Hierarchical Conformance Refinement Planning: An approach to ASP planning based on refinement which relaxes many of the limiting restrictions of existing techniques on both fronts;
  Novel highly versatile abstraction hierarchy representation allows for much larger variety of different abstract models for different domains,
  New flexible constraint based refinement method based on sub-goal planning alleviates the dependency problem that affect existing refinement planners.
Notes: Can divide problems into a sequence of smaller problems which shorter plan lengths which are then manageable to solve using ASP.

## Slide 8: Conformance Refinement Planning
Abstraction hierarchy containing arbitrary number of abstract models allows for progressive simplification of a domain/problem,
Abstract plans refined successively over an abstraction hierarchy, under simple constraint that requires that plans at different levels achieve the same effects and remain structurally similar.

## Slide 9: Conformance Refinement Planning
The abstract plans produce a sequence of fundamental sub-goal stages, that provide understanding of the structure of the plan at the original level, and increase planning speed from two properties;
  Conformance constraints formed by the sub-goal stages restrict search space,
  Optional division of problems to exponentially simpler partial-problems.

## Slide 10: Abstraction Hierarchies
Can represent of any form of abstraction that can be expressed logically and mapped to deterministically from the original model,
Two novel model types are contributed;
  Condensed models work by reducing size of state representation,
  Tasking models work by achieving a level of high-level task planning.
An abstraction hierarchy has to be designed for a specific domain,
The generality of a hierarchy is over different problems in the domain.
For complex domains, this hierarchy may be easier to obtain than an equivalent heuristic for classical planning, but only if there are properties of the domain that allow a hierarchy to be made.

## Slide 11: Conformance Refinement Planning
Primary benefits over existing ASP based planners;
  Maintains the expressivity and generality,
  Finds complete plans exponentially faster than existing ASP based planning,
  Ability to plan online reduces execution latency exponentially (to seconds).
Rarely finds the optimal plan but does find some plan of acceptable quality.
Most complex problem tested so far
  Initial partial solution found in ~12 seconds,
  Complete solution found in ~5 minutes,
  Estimated ~16% longer than optimal plan.
This cannot even be solved realistically by existing ASP planners, takes over an hour to reach half minimal plan length, with exponential trend.
Notes: There is a benefit to hierarchical planning that is intuitive to humans, that is that we usually only need an abstract plan, or rough idea of what we are going to do in the future as we start going, then we deal with the details as we go along, and as we discover more about what we are dealing with.
This is important in the real world, where a small loss in plan quality is acceptable, given that speed is of primary importance usually, people don’t want to wait around whilst the robot thinks.
I am tackling a group of problems that are usually not considered in most existing research, as they are considered intractable in general.
Introduces the interleaving property.
Allows combination of sub-problems that are dependent to achieve far better plan quality which only small reduction in speed via the.

## Slide 12: Progress and Changes
Planner implementation complete,
Currently running experiments and plan for thesis chapters/structure,
For the problems I have tested so far, I have managed to achieve the objective, and successfully combine ASP with refinement.
Due to time constraints I have removed;
  Diagnostics, re-planning, and plan repair,
  Multiple robots,
  Informed division strategies,
  Minimum step bound estimation,
  Scaled back to just one planning domain, but increased variety of problems.

## Slide 13: Conformance Refinement Planning
Finds complete plans exponentially faster than standard ASP based planning.
Yields partial plans exponentially faster than complete.
The abstract plan produces a sequence of fundamental sub-goal stages, that provide a substantial understanding of the structure of the plan at the original level, this guides search by allowing only plans that satisfy the constraint.
Primary benefits;
  Achieve good expressivity and generality,
  Very fast even for long plan lengths,
  Ability to plan online,
  Reduces execution latency to a matter of seconds,
Usually doesn’t find the optimal plan, but does find some plan of reasonable quality, in very little time.
Using a conformance constraint based approach we don’t have to refine each action separately, any contiguous sub-sequence of actions can be refined as a partial-problem, and dividing problems, which overcomes or alleviates the problems of existing refinement planning methods.
Allows combination of sub-problems that are dependent to achieve far better plan quality which only small reduction in speed via the interleaving property.
Notes: There is a benefit to hierarchical planning that is intuitive to humans, that is that we usually only need an abstract plan, or rough idea of what we are going to do in the future as we start going, then we deal with the details as we go along, and as we discover more about what we are dealing with.
This is important in the real world, where a small loss in plan quality is acceptable, given that speed is of primary importance usually, people don’t want to wait around whilst the robot thinks.
I am tackling a group of problems that are usually not considered in most existing research, as they are considered intractable in general.

## Slide 14: Abstraction Hierarchies
Versatility to find appropriate abstraction for wider range of domains.
Partial-problems defined by any contiguous sub-sequence of sub-goal stages;
  Allows combination of sub-problems that are dependent to achieve far better plan quality which only small reduction in speed via the interleaving property.
Sub-problems refine only one abstract action distinctly, producing a sub-plan, whereas partial-problems allow you to combine the refinement of multiple contiguous abstraction actions together to produce a partial-plan where the refinement of those actions can interleave.

## Slide 15: The Objective
Objective is to obtain a planner effective for very capable robots, to be deployed into our homes or work places, e.g. service robots.
Many fundamental unsolved problems towards this;
  Planning time and execution latency must be small be useful in real-world;
    Search space explodes exponentially with plan length in exhaustive search,
    Hard to obtain a general method to avoid this and still get good plans.
  Robots act with limited knowledge and observability in uncertain worlds;
    Robots need to be able to explore and learn from unknown domains/problems,
    Difficult to generate good quality plans that are likely to succeed and deal with failure.
This thesis tackles the plan generation process only.

## Slide 16: ASP Against Heuristic Planning
We want planners that are effective enough for really capable robot such as service robots, that are going to be deployed into our homes and work places to complete challenging tasks that previously could only be performed by humans.
ASP seems to have the capabilities to achieve this, but it is simply too slow, because the types of complex problems that it is well suited at representing, tend to have plan lengths that are simply too long for it to deal with.
Search space explodes exponentially with plan length in exhaustive search.
Classical heuristic planners have contrasting strengths;
  Not nearly as expressive or general, have poor elaboration tolerance (if you want to add one feature to the problem, you usually have to change many of the existing rules),
  Far better at dealing with long plan lengths iff accurate heuristic estimate can be found efficiently,
  This is because heuristics can massively reduce the potential search space, but in order to achieve this, the expressiveness of the encoding has to be limited to allow the heuristic to reason about properties that will exist in all possible encodings in a general manner,
  This is a design choice, heuristic planners have clear strengths and weaknesses, and these have been studied extensively,
  Heuristic planners can be really effective for real-world problems, if they are only dealing with a limited representation, path planning for example, sat-navs are extremely efficient.
If we want the benefits of ASP, we can’t rely on heuristics for two reasons;
  The types of problems that we would need ASP for are too complex to rely on heuristic guidance only,
  Heuristics are not appropriate for ASP based planning, they can be used, but they make the size of the logic program exponentially larger (increasing required memory usage exponentially),
  So if we want to get robots into complex real-world domains, we need to start looking at alternative approaches,
  A lot of research looks towards human reasoning techniques for inspiration, chief among these are machine learning based approaches which used prior experience to inform planning, and there are a large variety of approaches in the field, the others are those based on abstractions, these have generally been used in two ways, heuristics and hierarchical planning.
Unfortunately, many complex problems do have long plan lengths,
  This means that to date, there aren’t any ASP based planners that are particularly effective for any real-world uses, as they are intractable for most non-trivial problems.
ASP is effective for complex problems;
  Its reasoning capabilities allow it to deal with the exponential explosion in the search space with plan length when there are no heuristics
For problems that are sufficiently simple;
  Classical planners almost always out perform ASP based planners if there is an accurate and efficient heuristic that can be made.
Heuristics are not appropriate for ASP based planning, so for these problems ASP is not appropriate.
ASP does better that classical iff “good” heuristic estimates are not available, this usually happens when the problems are too complex to accurately of efficiently measure the distance to the goal, or where there are too many potential plans that have to be considered due to the large number of relevant entity constants.
The problem is that, the reason why good heuristics cannot be obtained is either because, the problem is too large/complex to make a good one, or there isn’t enough available knowledge to make a good one.
And the reason why classical planners are not that expressive is both because;
  It is hard to express state constraints in typical programming languages,
  They have to limit what can be expressed, to allow the heuristic to
Notes: Doesn’t need an explicit transition function to be defined, nor does it need a heuristic function. This is beneficial because it is very challenging to write those in such as way as to deal with complex state constraints in a way that is general.
ASP has the ability to reason with only the fundamental physical laws of the system, and be able to reason for itself to efficienctly find plans for complex combined problems, such as those with both navigation and manipulation, which can be challenging to write a heuristic function for because there is no clear measure of the distance to the shallowest goal state.
There are some pretty conclusive existing studies that show that ASP generally out performs the most efficient classical planners available for such problems, especially when there are large amounts of relevant entity constants, because it is extremely good at dealing with large knowledge bases.
But, for problems that are tractable for classical planners, but have long plan lengths, ASP usually doesn’t perform very well, because it cannot handle the exponential explosion in the search space was well as classical planners can if they have an effective heuristic.
Essentially, we can say that ASP based planners and classical planners have complimentary capabilities, but the problem is that heuristics are both not appropriate for ASP, nor are they particularly effective for complex problems, and they generally reduce generality and expressivity of domain encodings to allow for the heuristic to be able to efficiently obtain an accurate estimate.

## Slide 17: Sub-goal based planning
Describe what a complex combined problem/planning constraint actually is,
Describe why the approach is effective,
Use the Sussman anomaly as example of sub-goal based planning.
States - Start | Goal
Two different plans (transitions sequences)

## Slide 18: Sub-goal based planning
What sub-goals we actually want, and why these are effective.
This is when sub-goals are good, when they tell you something about the high level constraints/stages of the problem.
In this case, the problem is trivial, and the sub-goal stages almost effectively solve the problem, but in other cases, more extensive abstractions can produce similar effects of complex problems, where the order of completing/achieving critical stages operations as determined by the most fundamental of the domain/system’s laws can hugely guide search, as usually these constraints are the most challenging in finding a plan. This is the difference between path planning and most complete general (manipulation/combined) planning, the prior is essentially an optimisation problem, but that latter is a much more complex reasoning problem that needs to deal with a large number of complex constraints, and reasoning about the necessary operations, and in what order to do that to final a legal plan that reaches the final-goal state is much more challenging that in simple path planning, because the connections between the states (the legal state transitions) are much more complex to reason about that simple the connections between locations or nodes in the graph. We want to have guidance about the enabling constraints of actions that achieve the final-goal, and the enabling constraint of actions that enable those final-goal achieving actions.

## Slide 19: Fundamental decision making systems
Two highly interrelated decision making systems:
Division strategies | Online methods
Defines how to divide problems | Defines when problems are solved
You have to generate a division scenario every time you descend a level in the abstraction hierarchy,
You don’t have to complete each level before moving to the next,
Execution can only commence when the ground level is reached.

## Slide 20: Division Strategies
Naïve, informed, homogenous, heterogenous, favour speed, favour quality, proactive, reactive.
Complete-first tends to be good when using proactive favour quality for example, since you can see the whole complete level before making any divisions.
Divisions are there to reduce planning time and execution latency.
What do you want?
  Be able to measure the complexity of each problem,
  Be able to predict what sub-goals will be dependent with each other.